## Slide 1
CAPSTONE PROGRESS / NOTEBOOK WALKTHROUGH
AI-Based Voltage
Estimation Tutorials
The actual structure, code and outputs
A beginner-facing neural-network tutorial for electrical engineering students
Tutorial_1_LV_Voltage_Estimation.ipynb
PART 1
Neural Network-Based
LV Voltage Estimation
Build and evaluate the first model
Tutorial_2_MV_Effects_Reference_Voltage.ipynb
PART 2
MV Effects and
Reference Voltage
Diagnose and restore missing observability
Team Nando / Progress meeting / August 2026
Source: the two repository tutorial notebooks
01

## Slide 2
REPOSITORY STRUCTURE
The GitHub now contains two tutorial packages at different readiness levels.
xi/
Tutorial_1_LV_Vol_Estimation/
+-- Tutorial notebook.ipynb
+-- Exercise solutions.ipynb
`-- data / topology / search results
Tutorial_2_MV_Effects_Reference_Voltage/
+-- Tutorial notebook.ipynb
+-- Exercise solutions.ipynb
`-- fixed/MV data / network / saved results
CURRENT STATE
Part 1 tutorial
executed outputs
Part 1 solutions
executed outputs
Part 2 tutorial
executed; reads saved CSVs
Part 2 solutions
written; not yet executed
Source: repository tree and README.md
02

## Slide 3
PART 1 / NOTEBOOK STRUCTURE
01
Build and evaluate the first
neural network
Controlled upstream condition
2.3
Inspect the simulated dataset
2.3.5
Split time blocks and scale
2.4
Define model and training functions
2.5
Train, validate and select
2.6
Evaluate final test outputs
3
Complete three exercises
Notebook walkthrough: context -> code -> output -> learner exercise
Source: Tutorial 1 section headings
03

## Slide 4
PART 1 / 2.1 SIMULATED LV CIRCUIT
The first task is explicit: 62 P/Q inputs estimate 31 customer voltages.
31
single-phase customers
62
P/Q input values
->
neural-network mapping
31
voltage targets
Source: Tutorial 1, Section 2.1 and LVnetwork-topology.png
04

## Slide 5
PART 1 / DATA CONTRACT
Students verify every matrix before modelling.
REAL NOTEBOOK CODE / CELL 14
Observed shapes
TRAINING
6,048 x 62
P/Q inputs
6,048 x 31
voltage targets
FINAL TEST
2,016 x 62
P/Q inputs
2,016 x 31
voltage targets
0 invalid values found
Teaching move: make dimensions and data quality visible before any neural-network abstraction.
Source: Tutorial 1, Section 2.3, cell 14 output
05

## Slide 6
PART 1 / EXPLORE BEFORE TRAINING
Students inspect P, Q and V before training.
ONE DAY
Day 1
THREE CUSTOMERS
C1 / C16 / C31
LOOK FOR
When do load and voltage move together?
REAL NOTEBOOK OUTPUT / CELL 20
Source: Tutorial 1, Section 2.3.4, cell 20 output
06

## Slide 7
PART 1 / TIME-AWARE EVALUATION
Blocked time folds keep future samples out of training.
21-DAY TRAINING WINDOW
Fold 1
7 days
Fold 2
7 days
Fold 3
7 days
ISOLATED FINAL TEST
7 days / 2,016 samples
LEAKAGE GUARD
4,032
training samples
2,016
validation samples
Scalers fit on training only
REAL NOTEBOOK CODE / CELL 22
Source: Tutorial 1, Section 2.3.5, cell 22
07

## Slide 8
PART 1 / MODEL DEFINITION
The baseline network is small enough to understand line by line.
62
P/Q inputs
93 tanh
hidden units
31
voltage outputs
8,773
parameters
REAL NOTEBOOK CODE / CELL 24
Source: Tutorial 1, Section 2.4, cell 24
08

## Slide 9
PART 1 / TRAIN AND SELECT
Validation curves support an explicit model-selection decision.
REAL NOTEBOOK OUTPUT / CELL 34
SELECTED CONFIGURATION
155
hidden units
tanh
activation
1e-4
learning rate
2,000 epochs
CV RMSE 0.010986 V
Source: Tutorial 1, Section 2.5, cells 32-34
09

## Slide 10
PART 1 / FINAL TEST
The final test is reported as error, parity and customer-level risk.
Held-out 7-day test
0.01235 V
RMSE
0.00747 V
MAE
0.01646 V
90th-percentile absolute error
Worst customer
C24
customer RMSE 0.02553 V
REAL NOTEBOOK OUTPUT / CELL 44
Source: Tutorial 1, Section 2.6, cells 44-48
10

## Slide 11
PART 1 / PRACTICE AND SOLUTIONS
Exercises move from interpretation to model comparison and robustness.
E1
Interpret
Read profiles and explain where errors appear.
E2
Compare
Rank activation functions using validation RMSE.
E3
Stress-test
Repeat training across seeds and inspect stability.
SOLUTION NOTEBOOK OUTPUT / E2
The prompt is followed by an executable reference answer, so students can check both method and interpretation.
Source: Tutorial 1 exercise prompts and Tutorial 1 solutions, E2 output
11

## Slide 12
PART 2 / NOTEBOOK STRUCTURE
02
Stress-test what P/Q cannot observe
Same LV loading; altered upstream MV condition
2.3
Match P/Q; compare V
2.4
Isolate the MV effect
2.5
Test P/Q-only models
2.6
Add phase V references
2.7
Compare one scope
2.8
Estimate hosting capacity
3
Interpret the result
Controlled counterexample -> physical diagnosis -> added measurement -> engineering decision
Source: Tutorial 2 section headings
12

## Slide 13
PART 2 / CONTROLLED COUNTEREXAMPLE
P/Q differs by only 0.0074%, but voltage changes.
REAL NOTEBOOK OUTPUT / CELL 20
CONTROL CHECK
0.007412%
maximum relative P/Q difference
Notebook assertion
assert max_relative_diff
< 1e-4
Same P/Q does not imply
the same voltage.
Source: Tutorial 2, Section 2.3, cells 18 and 20
13

## Slide 14
PART 2 / PHYSICAL DIAGNOSIS
One subtraction reveals a 97.85% feeder-wide MV effect.
VARIANCE DECOMPOSITION
97.85%
feeder-wide component
2.15% phase component
0.00028% residual
Mean MV effect -1.3211 V
Standard deviation 0.5478 V
Source: Tutorial 2, Sections 2.4.1-2.4.2, cells 22 and 25
14

## Slide 15
PART 2 / FAILURE TEST
Linear and neural P/Q-only models both fail when MV is hidden.
Fixed MV
0.0128 V
Varying MV
0.6126 V
The shared failure is the lesson: this is an observability problem, not a neural-network victory.
Source: Tutorial 2, Section 2.5, cell 28 outputs
15

## Slide 16
PART 2 / RESTORE OBSERVABILITY
One voltage reference per phase restores RMSE to 0.0197 V.
ADD THREE MEASUREMENTS
C1
Phase A / voltage reference
C2
Phase B / voltage reference
C3
Phase C / voltage reference
Evaluate only C4-C31
P/Q only
0.6147 V
+ phase Vref
0.0197 V
96.8%
RMSE reduction
28 / 28 customers improve
Source: Tutorial 2, Section 2.7, cell 40 common-scope comparison
16

## Slide 17
PART 2 / ENGINEERING DECISION
Hosting-capacity error falls from +17.6% to +0.5%.
COMMON DECISION METRIC
4.841
kW / customer truth
5.693
P/Q only (+17.6%)
4.866
with phase Vref
+0.5% error
E3 prompt
Which estimator is unsafe, which is closest to truth, and why does Vref change the decision?
Source: Tutorial 2, Sections 2.8 and 3, cell 43 and Exercise 3
17

## Slide 18
CURRENT READINESS / NEXT SPRINT
The teaching arc exists; Part 2 now needs reproducibility and learner validation.
Artifact
Content
Outputs
Reproducible
Novice pilot
Part 1 tutorial
Part 1 solutions
Part 2 tutorial
Part 2 solutions
Ready
In progress
Pending
NEXT SPRINT
01
Integrate Part 2 data-generation scripts
02
Execute solutions and publish Colab path
03
Run a novice EE learner pilot
Current repository audit; readiness reflects notebook execution and learner-validation evidence
18

## Slide 19
BACKUP / PART 1 EVIDENCE
Selection and diagnosis remain inspectable beyond the headline RMSE.
ACTIVATION RANKING
RMSE BY CUSTOMER
WORST-CUSTOMER RESIDUAL
Backup sources: Tutorial 1 cells 46 and 48; Tutorial 1 solutions, Exercise 2
19

## Slide 20
BACKUP / PART 2 SENSITIVITY
Reference quality and proxy shift expose the limits of the recovery strategy.
REFERENCE COUNT, LOCATION AND NOISE
PROXY STRESS TEST
EXPLORATORY RESULTS
0.0825 V
at 0.05% meter noise
0.5579 V
288-slot proxy after a 2 h shift
Use these to teach sensitivity, not as the headline comparison: cells 34 and 37 use different evaluated scopes and feature setups from the formal C4-C31 result.
Backup sources: Tutorial 2 cells 34 and 37; exploratory scopes differ from cell 40
20

## Slide 21
BACKUP / REPRODUCIBILITY BOUNDARY
What the current repository evidence does - and does not - prove.
PART 1
Runs inside the notebook
- loads train/test P/Q and V
- trains and evaluates models
- renders diagnostics and exercise outputs
Clarify seed-CSV test provenance before release.
PART 2
Loads prepared evidence
- loads fixed-MV and varying-MV datasets
- reads precomputed result CSVs
- tutorial outputs are executed
Headline generation scripts are not yet in the repo.
SHARED LIMITATIONS
01
One simulated 31-customer feeder
02
One upstream variation pattern
03
No novice learner pilot yet
Backup source: repository and notebook execution audit
21